## Slide 1
Deposition Process
To grow WS2 films, a reactive sputtering process is implemented. In reactive sputtering, Argon atoms are ionized causing them to accelerate towards a negatively charged target. Upon hitting the Tungsten target, Tungsten atoms will be discharged and they will react with the gas in the chamber, Hydrogen Sulfide (H2S). This will then react and form WSX molecules that will be uniformly deposited onto a quartz slide. Between 1-5% H2S to Argon concentration and a pressure between 5-30mT will be tested. These values are adjusted to optimize the production process.
Growth of WS2 Thin Photovoltaic Films
Acknowledgments
We acknowledge the UCARE program, the Department of Electrical Engineering, and the University of Nebraska-Lincoln for funding the research. I also thank Dr. Natale Ianno and his graduate students for their guidance and expertise throughout this summer research program.
Matthew Hilfiker, Aaron Ediger, and Natale Ianno
Introduction
Through research for a material that is low cost, earth abundant, and highly efficient, Tungsten Sulfide (WS2) has been identified as a promising solution. From literature, it has been shown that WS2 possesses a band gap of 1.9 eV, which is ideal for a top layer heterostructure cell. While this is a favorable value, other properties needed to understand its value as a photovoltaic material are unknown. Through research, WS2 films will be grown through a sputtering deposition process and electrical characterization measurements will be performed to study these missing properties.
Results
The best results were produced by baking at 900°C for 20hrs. The XRD results are shown below along with the absorption plot. The peaks seen in the XRD correspond with the (002), (004), and (006) lattice for WS2 confirming WS2 was produced. The absorption plot verifies the band gap of WS2 of 1.85eV and no absorption is occurring below band gap indicating the absence of defect states in our material. The problem with these films is they do not stick to the quartz slide.
References
Ellmer, K. (2008). Preparation routes based on magnetron sputtering for tungsten disulfide (WS2) films for thin-film solar cells. Physica Status Solidi b 245 (9)
Ellmer, K., Stock, C., Diesner, K., Sieber, I. (1997) Deposition of CꞱ - oriented tungsten disulfide (WS2) films by reactive DC magnetron sputtering from a W-target in Ar/H2S. Journal of Crystal Growth. 182 (389-393)
Regula, M., Ballif, C., Remskar, M., Lévy, F. (1997) Crystallinity and texture promotion in WS2 films. J. Vac. Sci. Technol. A15, 2323
Interlock Safety Inc.; 11 April 2015; Web; 10 April 2016; Image.
Electrical Characterization Measurements
X-Ray Diffraction (XRD) allows us to verify our film microstructure. By calculating the intensity in which x-rays diffract across the sample, we can determine the size and shape of the unit cell, which is unique for each compound.
The UV-VIS spectrophotometer will be used to measure the absorption of the material. This will be used to verify the band gap of the material and quality WS2 is being produced.
Baking
The WSX films will be baked in a tube sealed at a pressure of 4.5E-7 Torr. This will be done to prevent oxygen from being present during this process so the films will be baked to the lowest energy state of hexagonal WS2. Baking temperatures will be experimentally tested between 800 and 900°C.
Department of Electrical Engineering, University of Nebraska, Lincoln, NE 68508
Conclusion
It was determined that 900°C for 20 hrs with an Al2O3 substrate was necessary to produce the highest quality WS2 films. Lower baking temperatures caused defects to be seen in both the XRD and absorption data. This production process is the first essential step into better understanding the properties of WS2 as a photovoltaic material. Work will be continued to perform electrical characterization measurements on these samples and the process of creating a WS2 solar cell device will be researched.
Tungsten Target
Film Growth Substrate
Ar+
Ar+
Chart: X-Ray Diffraction WS2 on Quartz
Ar+
W
W
W
W
W
W
W
W
S
S
S
S
S
W
S
W
H2S
+
↓
WSX
Chart: Direct Band Gap Absorption
Al2O3 Substrate Results
The XRD results are shown below for 20 hrs. at 900°C with an Al2O3 substrate. The XRD verifies that we can produce the same results as before but with the different substrate. Using these substrates a film that was able to fully stick to the substrate was produced.
WS2 (002)
Aluminum Oxide (Al2O3) Substrate
Aluminum Oxide substrates will be used instead of quartz to help the film in sticking. This is because Al2O3 has a thermal expansion coefficient of /°C which is closer to the expansion coefficient of WS2 than quartz which doesn’t expand.
Chart: X-Ray Diffraction WS2 with Al2O3 Substrate
WS2 (002)
WS2 (004)
WS2 (006)