## Slide 1
PRELIMINARY RESULTS & DISCUSSION
Leidenfrost Energy Barriers
James Peck, Anton Hassebrook, Craig Zuhlke,
Troy Anderson, Dennis Alexander, George Gogos, Sidy Ndao
Department of Mechanical Engineering, University of Nebraska–Lincoln
MOTIVATION
EXPERIMENTAL SETUPS
CONCLUSION & FUTURE WORK
ACKNOWLEDGEMENTS
FEMTOSECOND LASER SURFACE PROCESSING
LEIDENFROST ENERGY BARRIER THEORY
Self-propulsion of Leidenfrost droplets can be very important in microfluidics applications
Mechanisms causing self-motion of Leidenfrost droplets have been previously studied by our group using FLSP
Recently, our group discovered that there exists a barrier between two surfaces with different wettability near the Leidenfrost state
Understanding the fundamental mechanisms governing the Leidenfrost Energy Barrier will lead to better control of Leidenfrost droplets for microfluidics applications
Femtosecond Laser Surface Processing of polished Stainless Steel 304 sample to create super-hydrophilic region
SEM imaging of micro structures
Sample angled with a 1 degree incline sloping from the needle to the processed strip to draw liquid into barrier
50 trials of 4.17 µL deionized water droplets carried out for each temperature, with 5 degrees Celsius temperatures increments
Due to inconsistencies in droplet/barrier interactions from droplet bouncing, a new experimental setup will be used to test these Leidenfrost Energy Barriers
Figure 2. (A) Preliminary Energy Barrier Sample on Hot Plate. (B) New Energy Barrier Sample & Setup.
Figure 1. Mechanisms of Leidenfrost Droplet self-propulsion for ratchets and FLSP fish scales. Taken From: Kruse, et al., (2015). Microfluid Nanofluid. 18: 1418.
Figure 3. (A) Spectra-Physics Spitfire Laser. (B) Microstructure formation from preferential ablation, melting, fluid flow, and redeposition. (C) SEM image of FLSP microstructures
(A)
(B)
(C)
Figure 4. Boiling Regimes According to Nukiyama’s Boiling Curve. Image Taken From : Thermaodynamik. [Image]. http://129.187.45.233/tum-td/de/forschung/themen/subcooled_flow_boiling
This work has been supported by:
The UCARE program at the University of Nebraska - Lincoln
The Woollam Foundation and the Woollam Summer Internship Program
Nebraska Center for Energy Sciences Research (NCESR) with funds provided by Nebraska Public Power District (NPPD) to the University of Nebraska – Lincoln (UNL) No. 4200000844
NASA EPSCoR Grant # - NNX13AB17A
Department of Mechanical and Materials Engineering and the College of Engineering at UNL, awarded to SN.
Inconclusive results due to inability to prevent droplet bouncing with either experimental setup
Create new sample to minimize bouncing by using a square channel heated on all sides, utilizing the Leidenfrost effect on upper surface to repel bouncing droplets back towards channel floor
Determine droplet lifetime curves with deionized water on polished and processed surfaces of new sample to compare Leidenfrost Temperatures
Test the energy barrier concept by running Leidenfrost droplets into processed strip over a range of temperatures at and below the Leidenfrost temperature of the FLSP surface, while varying droplet mass and impact velocity
Leidenfrost temperature represents the maximum surface temperature at which efficient heat transfer can occur
It represents the onset of the film boiling regime
At the Leidenfrost point, a droplet floats on cushion of own vapor
At the Leidenfrost point, droplet lifetime is longest
The Leidenfrost temperature can be controlled by surface wettability of the substrate using FLSP
Leidenfrost Barrier can be created on a substrate with distinct surface regions having different Leidenfrost Points
With the sample heated to the Leidenfrost Point of the polished surface, the processed region will be in transition boiling
A droplet moving from the polished surface to the processed region will encounter a net force pushing it away from the processed region due to thrust from asymmetric boiling and wetting
As the Leidenfrost Point of the processed Energy Barrier was approached from below, the rejection percentage decreased
Highest rejection percentage of 54% occurred at Leidenfrost Point of polished surface region (275 Deg. C) - largest difference between sample temp. and processed region Leidenfrost Point.
Right side of the chart with rejection percentage below 10% corresponds to temperatures above Leidenfrost Point of processed surface
Wide variation in results observed from inconsistencies in droplet interactions with Energy Barrier from unpredictable droplet bouncing
Figure 6: Percent of droplets from preliminary set-up rejected from Barrier across a range of temperatures.
(A)
(B)
Figure 5. (A) Visualization of vapor flow field off Leidenfrost droplet near Energy Barrier (B) Images taken of a Leidenfrost droplet contacting the barrier and rejecting at a substrate temperature of 285 deg. C. The FLSP barrier is underlined in white.
.087 S
.100 S
.124 S
.164 S
(A)
(B)
Notes: Insert title for graph. Don’t forget to add border of 4.5pt font.
Implications
Study shows that cerium oxide coatings don’t give benefit to hydrophobicity, derive benefits from stainless steel and adding thermal resistance – overall no real benefit from coating